CITY OF WOONSOCKET, RHODE ISLAND

INVITATION TO BID FOR:

“WATER DISTRIBUTION SYSTEM MATERIALS” – BID# 6116

For the Woonsocket Water Department

Specifications are available at the Finance Department, Office of Purchasing, City of Woonsocket, 169 Main Street, Woonsocket, Rhode Island 02895 between the hours of 8:30 AM and 4:00 PM, Monday through Friday.

Sealed bids must be received, and date/time stamped by the City of Woonsocket, in the Finance Department, Office of Purchasing, City Hall, 169 Main Street, Woonsocket, Rhode Island no later than 11:00 A.M. on Wednesday, February 22, 2023.  Then, at the aforementioned date and time, on time bids will be publicly opened and read aloud in the 2nd Floor Conference room, City Hall, 169 Main Street, Woonsocket, Rhode Island.

ALL BIDS MUST BE SUBMITTED IN DUPLICATE COPY IN A SEALED ENVELOPE PLAINLY MARKED ON THE OUTSIDE OF THE ENVELOPE  “WATER DISTRIBUTION SYSTEM MATERIALS BID# 6116”.

BID SURETY IN THE FORM OF A CERTIFIED CHECK OR BID BOND IN THE AMOUNT OF 5% OF SUCH BID IS REQUIRED.

Individuals requesting interpreter services for the hearing impaired should call the Finance Director at 401-762-6400 seventy-two (72) hours in advance of the bid opening.

The City of Woonsocket reserves the right to reject any and all responses, or parts thereof, to waive any irregularity in the responses received and to accept the responses or parts thereof deemed to be most favorable to THE BEST INTEREST OF THE CITY.

Published:   February 8, 2023

_______________________

Christine Chamberland

Finance Director

INFORMATION TO BIDDERS

CITY OF WOONSOCKET

FINANCE DEPARTMENT

(401) 767-9269

1.	RECEIPT AND OPENING OF PROPOSALS:

Sealed bids/proposals will be accepted, and time stamped upon receipt in the Finance Department, Office of Purchasing, City of Woonsocket, 169 Main Street, Woonsocket, Rhode Island, 02895;  until the date and time, indicated on the attached Invitation to Bid, for the commodities, equipment or services listed in the specifications.  Bids/Proposals will be publicly read at the date and time specified in the Invitation to Bid.

2.	FORM OF BID:

Proposals shall be submitted in duplicate.  Supplemental information, drawings, warranties, literature, and material to be provided with the bid shall be on the bidder’s own form.

Where a specified brand or model number is asked for, it is to be viewed as a benchmark or standard, a substitute may be deemed equivalent at the discretion of the Finance Director.

The City of Woonsocket reserves the right to award a contract by item or in total.

3.	SUBMISSION OF BIDS:

- Envelopes containing bids must be sealed and addressed to the Finance Department, Office of Purchasing, City of Woonsocket, 169 Main Street, Woonsocket, Rhode Island 02895, and must be marked with the name and address of the bidder with the bid number and the name of the bid in the lower left-hand corner.

- If you are submitting a bid using a carrier such as FED EX, UPS, etc., the name of the bid and bid# must be marked on the envelope or label.

- The Finance Director will decide when the specified time has arrived to open bids and no bid thereafter will be considered.

- Any bidder may withdraw his bid by written request at any time prior to the advertised time for opening.  Telephone bids, faxed bids, amendments, or withdrawals will not be accepted.

- Unless otherwise specified, no bid may be withdrawn for a period of sixty (60) days from the time of bid opening.

- Negligence on the part of the bidder in preparing the bid confers no rights for the withdrawal of the bid after it has been opened.

- Proposals received prior to the time of opening will be securely kept, unopened.  No responsibility will be attached to an officer or person for the premature opening of a proposal not properly addressed and identified.

- Any deviation from the Specifications MUST BE NOTED IN WRITING AND ATTACHED AS PART OF THE BID PROPOSAL.  The bidder shall indicate how the bid will deviate from Specifications.

4.	RHODE ISLAND SALES TAX:

The City is exempt from the payment of the Rhode Island Sales Tax under the 1956 General Laws of the State of Rhode Island, 44-18-30, Paragraph 1, as amended.

5.	FEDERAL EXCISE TAXES:

The City is exempt from the payment of any excise tax or federal transportation taxes.  The price bid must be exclusive of taxes and will be so constructed.

6.	QUALIFICATION OF BIDDERS:

The City may make such investigations, as it deems necessary to determine the ability of the bidder to perform the work.  The bidder shall furnish the City with all such information and data for the purpose as may be requested.

7.	ADDENDA AND INTERPRETATIONS:

No interpretation on the meaning of the Plans, Specifications or other Contract Document will be made to any bidder orally.  Every request for such interpretations should be in writing, addressed to the Finance Director, P.O. Box B, Woonsocket, Rhode Island 02895, and to be given consideration must be received at least seven (7) days prior to the date fixed for the opening of the bids.  Fax transmissions will be accepted with written follow-up by bidder.

Any and all interpretations, and supplemental instructions which, if issued, will be mailed by regular mail to all perspective bidders (at the respective address furnished by the bidder for such purpose), not later than 48 hours prior to the date fixed for the opening of the bids (unless such addenda postpones the opening of bids).  Failure of bidder to receive any such addendum or interpretations shall not relieve any bidder from obligation under his bid as submitted.  All addenda so issued shall become part of the Contract Document.

8.	 DELIVERY:

All Purchases related to this bid are to be delivered FOB various locations within the City of Woonsocket, delivery to be supplied with the Purchase Order.  No extra charges for delivery, handling or other services will be honored.  Only inside delivery and set-up, where required, will be accepted.  TAILGATE DELIVERIES WILL BE REFUSED.  The vendor must notify the City of Woonsocket 24 hours prior to delivery.  All claims for damage in transit shall be the responsibility of the successful bidder.  The City will not make payment on damaged goods, they must be replaced or adjustments made at the option of the City.  The City of Woonsocket is only represented by the Finance Director in these matters and said director shall be the only entity to negotiate any settlements.  Deliveries must be made during normal working hours.

9.	Bid price is to include the cost of uncrating and setting in place where noted.

10.	Bid price is to include installation where noted.

11.	Bidder must comply with all State Labor Laws for Public Works projects.

- The successful bidder must have all current taxes paid which are owed to the City of Woonsocket.

# CITY OF WOONSOCKET

# RHODE ISLAND

# DEPARTMENT OF PUBLIC WORKS

CONTRACT DOCUMENTS   Bid # 6116

FOR

WATER DISTRIBUTION SYSTEM MATERIALS

SPECIFICATIONS

BID WORKSHEETS

AND

PROPOSAL

WATER DIVISION

FEBRUARY 2023

TABLE OF CONTENTS

I.	GENERAL SPECIFICATIONS

A.	OVERVIEW

B.	DELIVERY

C.	SUBMITTALS

II.	TECHNICAL SPECIFICATIONS

A.	REPAIR MATERIALS

1.	Cast couplings

2.	Water Repair Sleeves

3.	Alpha Restraint Coupling

B.	GATE VALVES

1.	Resilient Wedge

C.	TAPPING SLEEVES AND TAPPING VALVES

1.	Tapping Sleeve

2.	Tapping Valve

D.	HYDRANTS

- PIPE

##### BRASS FITTINGS (Corporations and Curb Stops)

#### COPPER TUBING

#### JOINT RESTRAINTS

I.  	GATE BOXES

##### J.	SERVICE BOXES

III.      BID WORKSHEETS  (BID QUANTITIES)

GENERAL SPECIFICATIONS

OVERVIEW

The service to be provided is the supply of repair, metering, and firefighting equipment.  The following specifications and quantities describe a possible fiscal year's supply of couplings, hydrants, valves, meters, and other water works materials.  Bidders shall construct a bid based on the specified quantities.  Each successful bidder will become sole supplier of some or all of these items during the 2024 fiscal year.  The water division does not guarantee to purchase the quantity of items specified; the quantities are merely a standard for comparing bids.  The successful bidders shall guarantee all prices quoted in the bid worksheets as well as specified delivery and technical requirements for all orders placed during the City of Woonsocket ‘s 2024 fiscal year (July 1, 2023 to June 30, 2024).

DELIVERY

Bidders shall indicate the estimated time of delivery.  The city reserves the right to reject any proposal having a long waiting time for delivery.  Immediate delivery may be required on repair materials of nominal sizes up to 12 inches and delivery within twenty-four (24) hours may be required on repair materials of sizes up to 36 inches.  The supplier shall provide a 24-hour phone number and contact person for emergency service.  Items which are not needed for emergency repair (valves, hydrants, meters, pipe, gate and service boxes) shall be delivered within four (4) weeks of an order.

The materials shall be delivered in high quality finished condition with acceptance subject to inspection and approval at the Water Crew Garage, 840 Cumberland Hill Road Woonsocket, Rhode Island 02895.  (2) Two-hour notice prior to delivery is required.  Delivery times are limited to Monday through Friday, 8AM to 3PM, excluding city holidays.

The materials shall be packaged and packed in accordance with good commercial practice to prevent damage during handling and shipment.

SUBMITTALS

Each bidder shall submit all bid worksheets and shall state the manufacturer and model number of each item to be supplied.  Bidders shall indicate products manufactured outside the U.S.A. Bidders shall supply manufacturer's literature for all proposed materials. Bidders shall note any deviations from technical specifications.

TECHNICAL SPECIFICATIONS

All of the following materials shall be rated for working pressures of at least 150 psi except repair sleeves above 10" NPS.  Any specified standards shall refer to the latest revision thereof.  All items specified with mechanical joint connections (e.g. couplings, valves, hydrants, elbows, tees, tapping sleeves, and crosses) shall include all necessary mechanical joint accessories (bolts, gasket, follower flange).  Bidders shall inform the Water Division of any errors they believe to exist in these technical specifications.

A.  REPAIR MATERIALS

1.	COUPLINGS

Couplings of 16” or smaller nominal size shall be of a gasketed, sleeve type with diameter to properly fit the specified pipe O.D. range.  Each coupling shall consist of one (1) cast (or ductile) iron middle ring, two (2) cast (or ductile) iron follower flanges, two (2) or more rubber compounded wedge section gaskets, and sufficient steel bolts, nuts etc.  Each coupling supplied shall comprise a full coupling assembly.

Product supplied shall conform to the part numbers in table 1.  Equivalent products by Dresser, Smith-Blair, or JCM shall be considered if submittals included with the bid fully establish equivalency.  Finished product shall meet AWWA standard C-219.

# TABLE 1 - COUPLINGS

| NOMINAL PIPE SIZE (IN.) | Smith-Blair Catalog Numbers | MINIMUM OD RANGE (IN.) | Minimum Sleeve Length (IN.) |
| --- | --- | --- | --- |
| 4 | 441-00000510-900 | 4.8 to 5.1 | 5 |
| 6 | 441-00000722-900 | 6.90 to 7.2 | 5 |
| 8 | 441-00000945-900 | 9.05 to 9.4 | 5 |
| 10 | 441-00001160-900 | 11.1 to 11.6 | 6 |
| 12 | 441-00001350-900 AND (2)GASKET 33821 | 13.2 to 13.75 | 6 |
| 14 | 441-00001550-900 AND (2)GASKET 33823 | 15.3 to 15.75 | 6 |

2.  WATER REPAIR SLEEVES

Water repair sleeves shall conform to the Smith Blair or JCM part numbers in the following table.  Equivalent types and/or models made by Smith Blair, Dresser or JCM shall be considered provided that a complete description is included to verify that their products are equal in usability and meet specification and standard requirements of all components.

The clamp band shall be stainless steel type 304.  The lugs shall be high strength ductile iron conforming to ASTM A536.  The gasket shall provide a leak proof seal and shall be compounded to resist oil, acids, alkalis, hydrocarbon fluids, water, and chemicals and to withstand temperatures between 30F and 212F.  The bolts shall be high strength low alloy steel conforming to ASTM A325 or A242 and the nuts shall conform to ASTM A563.  The repair sleeves shall be at least 12 inches wide for 4 inch, 6 inch, and 8 inch outside diameters and 15 inches wide for larger sizes.  The repair sleeves shall be suitable for the outside diameters specified in the following table.

TABLE 2, REPAIR SLEEVES

| NOMINAL PIPE SIZE (IN.) | Smith-Blair Catalog Numbers | JCM Catalog Numbers | MINIMUM OD RANGE (IN.) | Minimum Sleeve Length (IN.) |
| --- | --- | --- | --- | --- |
| 4 | 226-048012-000 OR 227-045012-000 OR 227-048012-000 | 101-0480-12 | 4.8 to 5.1 | 12 |
| 6 | 226-069012-000 OR 227-066312-000 OR 227-069012-000 | 101-0690-12 | 6.90 to 7.2 | 12 |
| 8 | 226-090512-000 OR 227-086312-000 OR 227-090512-000 | 102-0905-12 | 9.05 to 9.4 | 12 |
| 10 | 227-111015-000 | 102-1075-18 OR 102-1110-18 | 11.1 to 11.6 | 15 |
| 12 | 227-132015-000 | 102-1320-18 | 13.2 to 13.75 | 15 |
| 16 | 228-20171515-000 OR 228-20171520-000 | 102-1740-18 | 17.4 to 17.9 | 15 |
| 20 | 228-20215215-000 OR 228-20215220-000 | 102-2160-18 | 21.6 to 22.06 | 15 |
| 24 | 228-30257015-000 | 102-2580-18 | 25.8 to 26.32 | 15 |

3. ROMAC ALPHA RESTRAINED COUPLING

Description
Wide range restrained joint. Installs in about three minutes. Accommodates Ductile iron through IPS PVC pipe diameters. Manufactured in the U.S.A.

Nominal Sizes
4 - 12 inches.

Working Pressure
Up to 350 psi.

Application
Used to couple and restrain plain end pipe with different diameters within the range.

Pipe Compatibility
Ductile Iron
Cast Iron (Class A, B, C & D)
PVC IPS size (Sch 40, Sch 80 and SDR 21)
PVC C900 & C909
HDPE (SDR 9, 11, 13.5 & 17).

4.  ROMAC HP MACRO TWO-BOLT EXTENDED RANGE COUPLING

Nominal Sizes
2 - 12 inches.

Working Pressure
Up to 305 psi.

Application
Couple pipe ends with same or different diameters.

Pipe Compatibility
Ductile Iron, Steel, cast iron, asbestos cement, plastic and other types of pipes.

4. MECHANICAL JOINT GATE VALVES

Valves up to 12" NPS may be of the resilient wedge type.  Such valves shall be manufactured in accordance with AWWA Standard C509.  Valves shall be designed for 200 psi water working pressure.  Valves shall be mechanical joint type and shall have clear waterway equal to the full nominal diameter of the valve.  Valves shall be resilient wedge type with non-rising

stems, open right and provided with RED 2" square operating nuts.

Each Valve shall have "OPEN RIGHT," maker's name, pressure rating and year in which manufactured cast on body.  Prior to shipment from the factory each valve shall be tested by hydrostatic pressure of 400 psi. Valves shall be Kennedy 4571, Mueller 2360, or equal.

TAPPING SLEEVES AND TAPPING VALVES

5.  Tapping Sleeves (Cast Iron or Ductile Iron)

The tapping sleeves shall consist of a two-part casting of mechanical joint type, longitudinally flanged on the vertical centerline.  The entire surface area of each flange shall be machined.  The longitudinal flanges of the sleeves shall be fitted with a rubber gasket extending along their full length. A groove to receive the rubber gasket shall be provided on the inner surface of one of the longitudinal flanges of each half of the assembly.  The groove shall be located midway between the inside edge of the assembly and the bottom edge of the assembly boltholes.  When properly assembled, the flanges with the gasket grooves shall be located on opposite sides of the sleeve assembly horizontal and vertical centerlines.  The rubber gaskets shall provide watertight joints along the full length of the unit.  The bolts used to assemble the sleeve shall be closely spaced to ensure uniform gasket pressure and compression.

Sleeves shall be provided with a raised head at the base of each hub to aid in centering the sleeve or cross on the pipe.  The tapping sleeves shall be of the same manufacturer as the tapping valves with which they are to be used.

Sleeve outlets shall have counter bored flanges to ensure centering the tapping valve.

All materials shall be as specified in AWWA Standard C500 and the MSS-SP-60 detail.  The flange of the sleeve shall be faced and drilled to A.S.A. B16.1 Class 125 specifications and shall be delivered with all necessary bolts and gaskets.

Tapping sleeves shall be Mueller H-615, US Pipe T-9, or equivalents by Kennedy or Clow.

NOTE: Tapping sleeves incorporating a compression type O-ring seal are not acceptable.  Non-cast, fabricated sleeves made of stainless steel or other materials are not acceptable. Sleeves shall include all parts necessary to tap mains of the OD range specified for couplings.

6. Tapping Valves

Tapping valves shall conform to above specifications for gate valves except that one side shall be flanged for bolting to a tapping sleeve and the valve shall be compatible in every way with specified tapping sleeves and with all aspects of standard tapping procedures.

Valves shall be Kennedy C95OXR, Mueller H667, or equal.

7.  HYDRANTS

Hydrants shall be Mueller Super Centurion 250, Darling B-62b, or Kennedy K-81D only.  Hydrants shall open right and have a depth of bury at 5 1/2', 6’, or 6 1/2’ as specified.  Hydrant sections shall be a traffic model with breakaway coupling devices and main valve rod shall be connected at the ground line by a coupling.  The hydrant shall have an internal valve opening at least 5-1/4" in diameter and shall be equipped with a 4 1/2" pumper nozzle and two (2) 2 1/2" hose nozzles.  Threads and operating nut shall be National Standard.  The inlet connection shall be mechanical joint (bolts, gaskets, follower flanges, etc. shall be included). Hydrants shall be dry barrel, dry top design, and meet AWWA standard C-502.  Hydrant shoe shall be able to fit ductile iron and class "D" pit cast iron pipe.

8.  Ductile Iron Pipe

Class 52 Ductile Iron per AWWA Standard C-151, centrifugal cast.  Bell and spigot, using single elongated grooved rubber gasket similar and approved equal to the "Tyton" joint as manufactured by U.S. Pipe and Foundry Co.

Cement lined per AWWA C-104, except lining shall be not less than 1/8-inch thick (double thick).  Factory coated exterior w/coal-tar base coating and interior seal coated with same material.

9 & 10. Corporation Stops & Curb Stops

Brass Fittings Corporations and Curb-Stops (Stop and Waste Not Permitted) shall open right and be as manufactured by RED HED Manufacturing Company, Lincoln, RI.  Corporations shall conform to figure 438 & A and curb stops to figure 415 of the manufacturer’s literature.

### 11. COPPER TUBING

Copper tubing shall be type K, soft, of domestic manufacturer and conforming to the latest revision of the following specifications: Federal WW-T-799, ASTM B-88, AWWA 75-CR.  Copper tubing shall be supplied in continuous rolls of at least sixty feet long.

12. MECHANICAL JOINT RESTRAINED KITS

Joint restraints shall be as follows:

Mechanical joint restraint shall be incorporated in the design of the follower gland and shall include a restraining mechanism which, when actuated, imparts multiple wedging action against the pipe, increasing resistance as the pressure increases.  Flexibility of the joint shall be maintained after burial.  Glands shall be manufactured of ductile iron conforming to ASTM A536-80.  Restraining

devices shall be of ductile iron heat treated to a minimum hardness of 370 BHN.  Dimensions of the gland shall be such that it can be used with the standardized mechanical joint bell and tee head bolts conforming to ANSI/AWWA A21.11 and ANSI/AWWA C153/A21.53.  Twist off nuts shall be used to ensure proper actuating of the restraining devices.

13 GATE BOXES

Valve boxes shall be heavy pattern cast iron consisting of three components: an upper section, a lower section, and a cover.  The upper section shall slide over the lower section in a telescoping manner to provide sufficient lengths to accommodate various cover depths without traveling the full length of either section.  The top end of the upper section shall be flared outward to provide room for a recess on the inside diameter to receive the cover.  The cover shall be at least six inches in diameter and fit into the recess so that the top of the cover is flush with the rim edge of the top section.  The top end of the cover shall have the word “WATER” cast thereon in raised letters.  The cover shall fit into the recess in such a manner that would prevent the cover from “rattling” or from being dislodged and flipped out of the recess by contact with vehicular travel.  The bottom end of the top section shall be a plain end (not flanged).  The lower section shall be at least 5.25 inches inside diameter and belled or domed at the bottom to fit over the valve.

Valve boxes shall be of good quality cast iron, free from all defects in material and workmanship, and shall be coated over all surfaces (inside and outside) with coal-tar pitch enamel or other approved coating.  Valve boxes shall be “Buffalo” type suitable for the size valve on which they are used and shall be as manufactured by Buffalo Pipe and Foundry.  The top section shall be 24-inches long, the bottom section, 40-inches long.

The supplier must also be able to supply individual compatible components upon request.

13 SERVICE BOXES

Service boxes shall be heavy pattern cast-iron, cast in two telescoping sections of sliding construction and of such lengths as will provide the required cover, without full extension of either section.  The lower section shall be at least 2.5 inches inside diameter, belled or domed at the bottom to fit over the curb stop.  The upper section with lid flush with the top shall fit over the lower section.  Service boxes shall be of good quality, cast iron, free from all defects in material and workmanship, and shall be coated inside and outside with coal-tar pitch enamel or other approved coating.  Service boxes shall be “Buffalo” type and shall be as manufactured by Buffalo Pipe and Foundry, or an approved equal.  Each service box shall be complete with a top section and cover, a bottom section, rod, and centering ring. The top section shall be 24-inches long, the bottom section, 48-inches long, and the rod, 48-inches long.

The supplier must also be able to supply individual compatible components upon request.

City of Woonsocket, R.I.

III – BID# 6116    WORKSHEETS

| BOLTED COUPLINGS – WORKSHEET 1 |
| --- |
| SIZE | PRICE PER UNIT |
| 4” | One (1) for $ |
| 6” | One (1) for $ |
| 8” | One (1) for $ |
| 10” | One (1) for $ |
| 12” | One (1) for $ |
| 14” | One (1) for $ |
| 16” | One (1) for $ |
| TOTAL COUPLINGS PRICE | $ |

Coupling make(s) and model(s): _________________________________

Delivery Time: ___________________________

Signature: ___________________________

| WATER BREAK REPAIR SLEEVES – WORKSHEET 2 |
| --- |
| SIZE | PRICE PER UNIT |
| 4” | One (1) for $ |
| 6” | One (1) for $ |
| 8” | One (1) for $ |
| 10” | One (1) for $ |
| 12” | One (1) for $ |
| 14” | One (1) for $ |
| 16” | One (1) for $ |
| 20” | One (1) for $ |
| 24” | One (1) for $ |
| TOTAL REPAIR SLEEVE PRICE | $ |

Sleeve make(s) and model(s): ___________________________

Delivery Time: ___________________________

Signature: ___________________________

| ROMAC ALPHA COUPLINGS – WORKSHEET 3 |
| --- |
| SIZE | PRICE PER UNIT |
| 4 | One (1) for $ |
| 6 | One (1) for $ |
| 8 | One (1) for $ |
| 10 | One (1) for $ |
| 12 | One (1) for $ |
| TOTAL COUPLINGS PRICE | $ |

Coupling make(s) and model(s): _________________________________

Delivery Time: ___________________________

Signature: ___________________________

| ROMAC MACRO COUPLINGS – WORKSHEET 3 |
| --- |
| SIZE | PRICE PER UNIT |
| 4 | One (1) for $ |
| 6 | One (1) for $ |
| 8 | One (1) for $ |
| 10 | One (1) for $ |
| 12 | One (1) for $ |
| TOTAL COUPLINGS PRICE | $ |

Coupling make(s) and model(s): _________________________________

Delivery Time: ___________________________

Signature: ___________________________

| MECHANICAL JOINT GATE VALVES – WORKSHEET 4 |
| --- |
| SIZE (Inches) | PRICE PER UNIT |
| 4 | One (1) for $ |
| 6 | One (1) for $ |
| 8 | One (1) for $ |
| 10 | One (1) for $ |
| 12 | One (1) for $ |
| 14 | One (1) for $ |
| 16 | One (1) for $ |
| 20 | One (1) for $ |
| 24 | One (1) for $ |
| TOTAL GATE VALVE PRICE | $ |

Valve make(s) and model(s): ___________________________

Delivery Time: ___________________________

Signature: ___________________________

| TAPPING SLEEVES – WORKSHEET 5 |
| --- |
| SIZE | PRICE PER UNIT |
| 6” x 6” | One (1) for $ |
| 8” x 6” | One (1) for $ |
| 10” x 6” | One (1) for $ |
| 12” x 6” | One (1) for $ |
| 8” x 8” | One (1) for $ |
| 10” x 8” | One (1) for $ |
| 12” x 8” | One (1) for $ |
| TOTAL TAPPING SLEEVE PRICE | $ |

Tapping Sleeve make(s) and model(s): ___________________________

Delivery Time: ___________________________

Signature: ___________________________

| TAPPING VALVES – WORKSHEET 6 |
| --- |
| SIZE | PRICE PER UNIT |
| 6” | One (1) for $ |
| 8” | One (1) for $ |
| TOTAL TAPPING VALVE COST | $ |

Valve make(s) and model(s): ___________________________

Delivery Time: ___________________________

Signature: ___________________________

| HYDRANTS – WORKSHEET 7 |
| --- |
| DESCRIPTION | PRICE PER UNIT |
| 5 ½ FT BURY | $ |
| 6 FT BURY | $ |
| 6 ½ FT. BURY | $ |
| TOTAL COST OF HYDRANTS | $ |

Hydrant make and model: ___________________________

Delivery Time: ___________________________

Signature: ___________________________

| Ductile Iron Pipe – WORKSHEET 8 |
| --- |
| DESCRIPTION | UNIT PRICE |
| 6” CLDI PIPE | $ /ft. |
| 8” CLDI PIPE | $ /ft. |
| 10” CLDI PIPE | $ /ft. |
| 12” CLDI PIPE | $ /ft. |
| TOTAL COST OF PIPE | $ |

Pipe manufacturer: ___________________________

Delivery Time: ___________________________

Signature: ___________________________

| CORPORATION STOPS – WORKSHEET 9 |
| --- |
| SIZE (Inches) | PRICE PER UNIT |
| .75 | One (1) for $ |
| 1 | One (1) for $ |
| 1.5 | One (1) for $ |
| 2 | One (1) for $ |
| TOTAL CORPORATION STOP PRICE | $ |

Corporation make(s) and model(s): ___________________________

Delivery Time: ___________________________

Signature: ___________________________

| CURB STOPS – WORKSHEET 10 |
| --- |
| SIZE | UNIT PRICE |
| 3/4” | $ |
| 1” | $ |
| 1 ½ “ | $ |
| 2” | $ |
| TOTAL CURB STOP PRICE | $ |

Curb Stop make(s) and model(s): ___________________________

Delivery Time: ___________________________

Signature: ___________________________

| COPPER TUBING – WORKSHEET 11 |
| --- |
| DESCRIPTION | UNIT PRICE |
| ¾” Copper Tubing | $ /ft. |
| 1” Copper Tubing | $ /ft. |
| 1 ½” Copper Tubing | $ /ft. |
| 2” Copper Tubing | $ /ft. |
| TOTAL COST OF Copper Tubing: $ |

Copper Tubing Manufacturer: ___________________________

Delivery Time: ___________________________

Signature: ___________________________

| JOINT RESTRAINT KITS COMPLETE – Follower, Gasket and Bolts WORKSHEET 12 |
| --- |
| SIZE (NPS) | UNIT PRICE | TOTAL PRICE PER QUANTITY |
| 4 | $ | One (1) for $ |
| 6 | $ | One (1) for $ |
| 8 | $ | One (1) for $ |
| 10 | $ | One (1) for $ |
| 12 | $ | One (1) for $ |
| TOTAL JOINT RESTRAINT PRICE | $ |

Joint Restraint make(s) and model(s): ___________________________

Delivery Time: ___________________________

Signature: ___________________________

| SERVICE AND GATE BOXES – WORKSHEET 13 |
| --- |
| (1) | GATE BOX | $ |
| (1) | COMPLETE SERVICE BOX Rods & CENTERING Rings | $ |
| TOTAL COST OF GATE & SERVICE BOXES | $ |

Service / Gate Box mfg.: ___________________________

Delivery Time: ___________________________

Signature: ___________________________

CITY OF WOONSOCKET, RHODE ISLAND

DEPARTMENT OF PUBLIC WORKS

PROPOSAL

Having familiarized ourselves with the above specifications, we submit the following totals for competitive bidding comparison:

TOTAL FROM WORKSHEET 1                         PRICE $___________

TOTAL FROM WORKSHEET 2                         PRICE $___________

TOTAL FROM WORKSHEET 3                         PRICE $___________

TOTAL FROM WORKSHEET 4                         PRICE $___________

TOTAL FROM WORKSHEET 5                         PRICE $___________

TOTAL FROM WORKSHEET 6                         PRICE $___________

TOTAL FROM WORKSHEET 7                         PRICE $___________

TOTAL FROM WORKSHEET 8                         PRICE $___________

TOTAL FROM WORKSHEET 9                         PRICE $___________

TOTAL FROM WORKSHEET 10                        PRICE $___________

TOTAL FROM WORKSHEET 11                        PRICE $___________

TOTAL FROM WORKSHEET 12                        PRICE $___________

TOTAL FROM WORKSHEET 13                        PRICE $___________

TOTAL FROM WORKSHEET 14                        PRICE $___________

TOTAL FROM WORKSHEET 15                        PRICE $___________

TOTAL BID AMOUNT (TOTAL OF ALL WORKSHEETS) PRICE $________________

TOTAL BID AMOUNT (TOTAL OF ALL WORKSHEETS) STATED IN WORDS:

____________________________________________________________________

| PROPOSAL SUBMITTED BY: Company Name: ________________________________________________________________ |
| --- |
| Address: _____________________________________________________________________ City/State/Zip Code _____________________________________________________________ |
| Representative: _________________________________ | Phone: _______________________ |
| Signature: _____________________________________ | 24 hr. Phone: __________________ |
| Email address: __________________________________ | Fax No: _______________________ |